## Slide 1: Stability of subcritical electrohydrodynamics in dielectric fluids
Mengqi Zhang
Institut Pprime, University of Poitiers
in collaboration with
  Fulvio Martinelli, Jian Wu, Peter J. Schmid and Maurizio Quadrio
IWEHD, Poitiers 2016

## Slide 2: Outline
Motivation
Methodology: linear and weakly nonlinear stability
Results
Conclusions and perspectives

## Slide 3: Motivation

## Slide 4: Various applications of EHD in industry
Motivation
Flow control
Electrospinning
Electrospray
Electrostatic
Precipitator
Mixing

## Slide 5: Methodology

## Slide 6
Geometry
Strong injection
Hydrostatic EHD:
No cross-flow
Poiseuille-EHD:
with cross-flow
We use simple geometry
(two infinite plate electrodes)
to investigate
the essential flow dynamics
Injected ions
Fluid particles

## Slide 7: Mathematical tools

## Slide 8: Linear stability analysis

## Slide 9
Linear stability analysis
Navier-Stokes equation:
Governing equation for the potential:
Modal | Non-modal
Instability/stability in the asymptotic time as an eigenvalue problem | Transient growth in a short time as an initial value problem
Normal operator: L*L = LL* (the eigenfunctions are orthogonal to each other) | Non-normal operator: L*L ≠ LL* (the eigenfunctions are not orthogonal to each other)
*: complex-conjugate
Linear stability analysis
Schmid & Henningson (2001)
Trefethen & Embree (2005)
Schmid (2007)

## Slide 10
>1, energy growth
<1, energy decay
1
Red: linear
operator
Blue: its
eigen-
expansion
0
Stable orthogonal modes decaying at different rates
Linear stability analysis: normal operator
Linear stability analysis: normal operator

## Slide 11
1
Red: linear
operator
Blue: its
eigen-
expansion
0
>1, energy growth
<1, energy decay
Stable non-orthogonal modes decaying at different rates
In the case of shear flow…..,
Linear stability analysis: non-normal operator
Linear stability analysis: non-normal operator
Growth/decaying rate
(modal/non-modal
stability analysis)
Transient growth
(non-modal stability
analysis)

## Slide 12
In the case of shear flow…..,
Linear stability analysis: non-modal analysis
Flow types (Shear flows) | Critical Reexp | Critical Relin
Pipe flow | ~ 2000 | ∞
Plane Couette flow | ~ 360 | ∞
Plane Poiseuille flow | ~ 1000 | 5772
Flow types | Critical Texp | Critical Tlin
EHD flow (SCL) | ~ 100 | 160.75
?
Schmid &
Henningson (2001)
Atten & Moreau
(1972)
what about the non-modal effect in EHD？
Linear stability analysis: non-modal analysis
by modal linear
stability analysis

## Slide 13: Weakly nonlinear stability analysis

## Slide 14: Weakly nonlinear stability analysis
Weakly nonlinear stability analysis
Multiple-scale expansion method
Stewartson & Stuart (1971)
1.Substitution
2.Regrouping

## Slide 15: Weakly nonlinear stability analysis
Weakly nonlinear stability analysis
Ginzburg-Landau equations
Linear problem
Solvability conditions

## Slide 16: Weakly nonlinear stability analysis
Weakly nonlinear stability analysis
Ginzburg-Landau equations
Supercritical bifurcation
Subcritical bifurcation
Guckenheimer & Holmes (1983)

## Slide 17: Results

## Slide 18: The cases studied
Linear stability
analysis (3D)
Weakly nonlinear
stability analysis (2D)
Hydrostatic EHD flow
Poiseuille-EHD flow
Hydrostatic EHD flow
Poiseuille-EHD flow

## Slide 19
C: charge injection level.
M: ratio between hydrodynamic mobility and the ion mobility.
T: electric Rayleigh number.
Fe: the inverse of electric charge diffusion coefficient. 1/Fe.
Re: Reynolds number.
: streamwise wavenumber
: spanwise wavenumber
Parameters in the problems

## Slide 20: Linear stability analysis of hydrostatic EHD flow
Linear stability
analysis (3D)
Weakly nonlinear
stability analysis (2D)
Hydrostatic EHD flow
Poiseuille-EHD flow
Hydrostatic EHD flow
Poiseuille-EHD flow

## Slide 21: Effect of charge diffusion 1/Fe （neutral stability curves in -T plane）
Charge
diffusion
coefficient
Tc=160.75
The stronger charge diffusion effect, the more unstable the flow is.
Linear stability analysis: hydrostatic EHD flow
C=50, M=100

## Slide 22: Effect of charge diffusion （transient growth）
Linear stability analysis: hydrostatic EHD flow
The stronger charge diffusion, the higher transient growth.
But the transient growth is in general very small in hydrostatic EHD.
C=50, M=100, T=155, =2.5

## Slide 23: Effect of mobility ratio M （neutral stability curves in M-T plane）
Linear stability analysis: hydrostatic EHD flow
C=100, Fe=105
The mobility ratio does not affect the linear stability criterion Tc.

## Slide 24: Effect of mobility ratio M （transient growth）
Linear stability analysis: hydrostatic EHD flow
C=50, Fe=105, T=155, =2.57
The mobility ratio does affect the transient growth. Higher M, smaller transient growth.

## Slide 25
Conclusions
Linear stability analysis for hydrostatic EHD:
Stronger charge diffusion will make the EHD flow more unstable
The non-modal effect in hydrostatic EHD is generally small, so it probably cannot explain the discrepancy between the theoretical Tc and the experimentally-determined Tc.

## Slide 26
Linear stability analysis of
Poiseuille-EHD flow
Linear stability
analysis (3D)
Weakly nonlinear
stability analysis (2D)
Hydrostatic EHD flow
Poiseuille-EHD flow
Hydrostatic EHD flow
Poiseuille-EHD flow

## Slide 27
Linear stability analysis: transition to turbulence in Poiseuille flow
Fully developed turbulence
Streaks breakdown
Streaks formation
Low-speed streaks
High-speed streaks
Turbulence spot
Non-modal linear stability analysis
Schmid & Henningson (2001)

## Slide 28
Linear stability analysis: lift-up mechanism
z
y
Poiseuille flow:
Streamwise rolls
Low-speed streaks
High-speed streaks
In non-modal stability analysis
the optimal initial conditions:
Streamwise wavenumber =0
Spanwise wavenumber =2.05
Base flow
Optimal perturbation

## Slide 29
Linear stability analysis: transition to turbulence in Poiseuille flow
Fully developed turbulence
Streaks formation
The streaky structure in the transition to turbulence process can be predicted successfully by the non-modal linear stability analysis. This process is coined lift-up mechanism.
Streaks breakdown
Turbulence spot

## Slide 30
Linear stability analysis: transition to turbulence in Poiseuille flow
Fully developed turbulence
Streaks formation
The streaky structure in the transition to turbulence process can be predicted successfully by the non-modal linear stability analysis. This process is coined lift-up mechanism.
Streaks breakdown
Turbulence spot
V
E
?
What’s the impact of EHD on
the lift-up mechanism?

## Slide 31: Effect of electric Rayleigh T （neutral stability curves in -Re plane）
With increasing T, the Poiseuille-EHD flow destabilises.
Linear stability analysis: Poiseuille-EHD flow
Rec=5772.22
C=100, Fe=105, =0

## Slide 32: Effect of electric Rayleigh T （transient growth）
The transient growth is quite large due to the lift-up mechanism.
The electric field enhances its growth.
C=100, Fe=105, Re=5200, =0, =2
Linear stability analysis: Poiseuille-EHD flow

## Slide 33
Linear stability analysis: enhanced lift-up mechanism
Poiseuille flow:
symmetric
Poiseuille-EHD flow:
asymmetric due to
the electric field
z
y
y
Optimal initial conditions:
Streamwise wavenumber =0
Spanwise wavenumber =2.36
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
z
E
effect of the electric field on lift-up mechanism: streamwise rools
Spanwise wavenumber =2.05

## Slide 34
The electric field makes it easier to form the streaky structures:
enhanced lift-up mechanism.
Linear stability analysis: enhanced lift-up mechanism
z
V
E
Lower low-speed streaks
Higher high-speed streaks
y
When the electric field is imposed, due to the drift velocity…
Injector
Collector
effect of the electric field on lift-up mechanism: streaks
+
+
+
+
+

## Slide 35
Conclusions
Linear stability analysis for hydrostatic EHD:
Stronger charge diffusion will make the EHD flow more unstable
The non-modal effect in hydrostatic EHD is generally small, so it probably cannot explain the discrepancy between the theoretical Tc and the experimentally-determined Tc.
Linear stability analysis for Poiseuille-EHD:
The lift-up mechanism, which is a powerful energy growth route in Poiseuille flow, is enhanced by the electric field in the Poiseuille-EHD flow.

## Slide 36
Weakly nonlinear stability analysis of
hydrostatic EHD flow
Linear stability
analysis (3D)
Weakly nonlinear
stability analysis (2D)
Hydrostatic EHD flow
Poiseuille-EHD flow
Hydrostatic EHD flow
Poiseuille-EHD flow

## Slide 37: Effect of mobility ratio M
The higher M, the stronger destabilizing effect of nonlinearity (higher positive a3).
Weakly nonlinear stability analysis: hydrostatic EHD flow
C=50, Fe=103, at the critical condition
Wu et al. (2015)
DNS

## Slide 38: Effect of charge diffusion 1/Fe
The weaker the charge diffusion, the stronger the destabilizing effect of nonlinearity (higher positive a3).
C=12.5, M=100, at the critical condition
Weakly nonlinear stability analysis: hydrostatic EHD flow
The critical finite-amplitude Tf
In previous prediction of Tf
No charge diffusion
Actual charge diffusion
(103<1/Fe<104)
destabilizing less!
Tf with charge diffusion > Tf without charge diffusion

## Slide 39
Conclusions
Linear stability analysis for hydrostatic EHD:
Stronger charge diffusion will make the EHD flow more unstable
The non-modal effect in hydrostatic EHD is generally small, so it probably cannot explain the discrepancy between the theoretical Tc and the experimentally-determined Tc.
Linear stability analysis for Poiseuille-EHD:
The lift-up mechanism, which is a powerful energy growth route in Poiseuille flow, is enhanced by the electric field in the Poiseuille-EHD flow.
Weakly nonlinear stability analysis for hydrostatic EHD:
In the weakly nonlinear phase, the stronger charge diffusion will less destabilize the flow, but the higher mobility ratio will more destabilize the flow.
The actual Tf should be higher than the values predicted in the previous works without taking into account the charge diffusion effect (which destabilizes less).
Castellanos et al. (1989)

## Slide 40
Weakly nonlinear stability analysis of
Poiseuille-EHD flow
Linear stability
analysis (3D)
Weakly nonlinear
stability analysis (2D)
Hydrostatic EHD flow
Poiseuille-EHD flow
Hydrostatic EHD flow
Poiseuille-EHD flow

## Slide 41: Effect of electric Rayleigh T
The higher the T, the stronger the weakly nonlinear effect destabilizing the flow, i.e., the Poiseuille-EHD flow is more subcritical than the conventional Poiseuille flow.
C=50, Fe=103, at the critical condition
=30.96
Weakly nonlinear stability analysis: Poiseuille-EHD flow

## Slide 42: Which part of the nonlinearity destabilizing the flow?
Weakly nonlinear stability analysis: Poiseuille-EHD flow

## Slide 43
Third-order nonlinear terms in the governing equation for the streamfunction
Third-order nonlinear terms in the governing equation for the electric potential
Weakly nonlinear stability analysis: Poiseuille-EHD flow

## Slide 44
Third-order nonlinear terms in the governing equation for the streamfunction
Poiseuille flow
Poiseuille flow
Poiseuille-EHD flow
Poiseuille-EHD flow
The enhanced subcriticality of Poiseuille-EHD flow results from the modified hydrodynamic part (streamfunction), rather than directly from the electric potential.
Third-order nonlinear terms in the governing equation for the electric potential
C=50, Fe=103, at the critical condition
Weakly nonlinear stability analysis: Poiseuille-EHD flow

## Slide 45
Conclusions
Linear stability analysis for hydrostatic EHD:
Stronger charge diffusion will make the EHD flow more unstable
The non-modal effect in hydrostatic EHD is generally small, so it probably cannot explain the discrepancy between the theoretical Tc and the experimentally-determined Tc.
Linear stability analysis for Poiseuille-EHD:
The lift-up mechanism, which is a powerful energy growth route in Poiseuille flow, is enhanced by the electric field in the Poiseuille-EHD flow.
Weakly nonlinear stability analysis for Poiseuille-EHD:
The Poiseuille-EHD flow becomes more subcritical than the conventional Poiseuille flow,
and the enhanced subcriticality comes from the modified streamfunction, rather than directly from the electric effect. So we can infer that it is important to calculate correctly the hydrodynamic field.
Traoré & Wu (2013)
Weakly nonlinear stability analysis for hydrostatic EHD:
In the weakly nonlinear phase, the stronger charge diffusion will less destabilize the flow, but the higher mobility ratio will more destabilize the flow.
The actual Tf should be higher than the values predicted in the previous works without taking into account the charge diffusion effect (which destabilizes less).
Castellanos et al. (1989)

## Slide 46
Weakly nonlinear stability analysis for Poiseuille-EHD:
The Poiseuille-EHD flow becomes more subcritical than the conventional Poiseuille flow,
and the enhanced subcriticality comes from the modified streamfunction, rather than directly from the electric effect. So we can infer that it is important to calculate correctly the hydrodynamic field.
Conclusions
Linear stability analysis for hydrostatic EHD:
Stronger charge diffusion will make the EHD flow more unstable
The non-modal effect in hydrostatic EHD is generally small, so it probably cannot explain the discrepancy between the theoretical Tc and the experimentally-determined Tc.
Linear stability analysis for Poiseuille-EHD:
The lift-up mechanism, which is a powerful energy growth route in Poiseuille flow, is enhanced by the electric field in the Poiseuille-EHD flow.
Traoré & Wu (2013)
Weakly nonlinear stability analysis for hydrostatic EHD:
In the weakly nonlinear phase, the stronger charge diffusion will less destabilize the flow, but the higher mobility ratio will more destabilize the flow.
The actual Tf should be higher than the values predicted in the previous works without taking into account the charge diffusion effect (which destabilizes less).
Castellanos et al. (1989)

## Slide 47
These works have been published recently in
M. Zhang, F. Martinelli, J. Wu, P. J. Schmid and M. Quadrio. Modal and nonmodal stability analysis of electrohydrodynamic flow with and without cross-flow. Journal of Fluid Mechanics, 770, 319-349, 2015
M. Zhang, Weakly nonlinear stability analysis of subcritical electrohydrodynamic flow subject to strong unipolar injection. Journal of Fluid Mechanics, 792, 328–363, 2016

## Slide 48
Perspectives
Perspectives on the future works of the stability analysis of EHD flow
Transition to turbulence in hydrostatic EHD flow.
The pattern formation of hydrostatic EHD flow.
Convective/absolute instability in the Poiseuille-EHD system.
How does the electric field affect the turbulence in Poiseuille flow? The auto-generation cycles. Drag reduction by EHD.
Carrière & Monkewitz (1999) for Poiseuille-RBC
Atten & Lacroix(1979) for infinite M
Schmid & Henningson (2001)
Drazin & Reid (2004)
Soldati & Banerjee (1998)
Hamilton et al. (1995)

## Slide 49: Thank you for your attention!