## Slide 1
UMSE
ELECTRODE ARRANGEMENT IMPACT ON HEAT TRANSFER IN HORIZONTAL CHANNELS
Rahma Gannoun, Walid Hassen, Mohamed Naceur Borjini, Habib Ben Aissia
Research Unit of metrology and energy systems, National School of Engineers of Monastir
FIRST INTERNATIONAL WORKSHOP ON ELECTRO-HYDRO-DYNAMICS AND TRIBO-ELECTROSTATICS

## Slide 2
What is Electrohydrodynamic (EHD)
EHD is an interdisciplinary field dealing with the interaction of fluids and electric fields or charges
Simple devices
The size of the device is small and the shape and the size of the electrodes can be easily adjusted
The flow responds rapidly to the applied electric field
Lower power consumption and noise
High efficiency in the case of small temperature difference
Promising opportunities in heat transfer enhancement
Electric energy
Kinetic energy
Notes: Then from this simple definition, we can conclude that if we apply an electric field to a fluid confined in a cavity, creating a potential difference, we will generate a movement so there is a transit from electric energy to kinetic energy
EHD presents many advantages
Based on all these advantages, EHD presents promising apportunities in heat transfer enhancement

## Slide 3
Objectives
Resolution of the problem of electro-thermo-convection ( electro-convection coupled with heat transfer) in horizontal channels
The majority of the researches done until now are either theoretical or experimental, however the complete resolution of equations modeling the problem is still very rare
Effect of electrodes’ arrangement on heat transfer
Characteristics of the flow and heat transfer in conjunction with Rayleigh number, electric Rayleigh and electrodes position

## Slide 4
Generator
Dielectric fluid
(ε, K)
Potential
Difference
ΔV =V0-V1
Temperature Difference
Δθ =θC-θF
θC
θF
Problem Geometry

## Slide 5
Energy equation
Navier Stokes equation
charge
conservation
Maxwell Gauss equation
equation
Defining the electric field
Continuity Equation
Mathematical formulation

## Slide 6
Electric forces
Current density
Mathematical formulation

## Slide 7
For universal and convenient description, it is customary to work with dimensionless equations and for this we introduce the dimensionless following quantities :
To simplify the calculation including the existence of the term of the pressure that appears in the Navier Stokes we had recourse to formalism "vorticity - stream function" (ψ-ω)
Mathematical formulation

## Slide 8
Mathematical formulation

## Slide 9
Ra Rayleigh number: characterizes the heat transfer mode in a fluid
Mathematical formulation

## Slide 10
Prandtl number Pr: represents the ratio of the diffusivity of momentum and thermal diffusivity
Mathematical formulation

## Slide 11
T number of electric Rayleigh: the ratio of the Coulomb force and the viscous forces
Mathematical formulation

## Slide 12
The dimensionless number C which measures the level of injection
Mathematical formulation

## Slide 13
The dimensionless number M represents electro-hydrodynamic properties of the fluid
Mathematical formulation

## Slide 14
We define, for convenience electrical Reynolds R
Mathematical formulation

## Slide 15
Electrodes asymmetrically placed on the left side
Electrodes placed equidistanly on either side of the center of the channel
Electrodes arrangement (Pr=0.72, Ra=104, C=10, M=10, N=4)
Four different configurations
Adjoined Electrodes
Spaced electrodes

## Slide 16
T=200
T=500
T=800
T=1200

## Slide 17
Emitting wall is gaining charges progressively
When T exceeds 200 , this parameter has no more effect on the receiving wall
Results: first electrodes’ arrangement (Pr=0.72, Ra=104, C=10, N=2)
T=200
T=500
T=800
T=1200

## Slide 18
Results: second electrodes’ arrangement (Pr=0.72, Ra=104, C=10, N=2)
Charges reaching the entire vertical left wall
T=200
T=500
T=800
T=1200
Wider mushrooms when increasing T

## Slide 19
Results: third electrodes’ arrangement (Pr=0.72, Ra=104, C=10, N=2)
T=200
T=500
T=800
T=1200

## Slide 20
Results: fourth electrodes’ arrangement (Pr=0.72, Ra=104, C=10, N=2)
T=200
T=500
T=800
T=1200
Increasing T allows the narrowing of the surface covered with charges of the emitting wall

## Slide 21
Nusselt number in function of electric Rayleigh for different electrodes arrangement
There is a 31% increase in heat transfer comparing the conventional natural convection case and T=1200
Either symetrically or not, bonded electrodes provide the lowest Nu
For high T value electrodes symmetrically bonded position 3) achieve greater heat transfer
Heat transfer enhancement achieved by electrode arrangement can reach up to 13% (position 2)
Results: heat transfer

## Slide 22
Numerical simulations are performed to analyze the mechanism of natural convection inside horizontal channels incorporating an electrohydrodynamic effect induced by narrow strip electrodes
Compromise should be put between electric Rayleigh, number of electrodes and convenient electrode arrangement
Conclusion
The flow pattern and charge density distribution are affected by the provided electric Rayleigh
placing electrodes symmetrically bonded should be avoided